## Slide 2: Introduction
Low power and Lossy Networks are resource constrained
WSN, IoT and Cyber-Physical System(CPS) are characterized as LLNs because nodes in such networks possess limited resources and often operate in harsh communication environments, resulting in transmission losses over wireless links
Routers are usually limited in terms of processing power, battery and memory and their interconnects are characterised by unstable links with high loss rates, low data rates and low packet delivery rates.
The traffic patterns could be P2P or P2MP or MP2P
Lossy means the packet drop rate will be high

## Slide 3: Introduction
RPL is a distance vector routing protocol
It mainly targets collection-based networks where nodes periodically send measurements to a collection point.
The protocol was designed to be highly adaptive to network conditions and to provide alternate routes, whenever default routes are inaccessible
RPL provides a mechanism to disseminate information over the dynamically formed network topology.
Contains thousands of nodes

## Slide 4: RPL topology
DODAG – Destination Oriented Directed Ayclic Graphs
  It is a DAG rooted at a single destination. The DODAG root has no outgoing edges. A DODAG is uniquely identified by a combination of RPL instance ID and DODAG ID
Rank
  A nodes Rank defines the nodes individual position relative to other nodes with respect to a DODAG root. Rank strictly increases in the Down direction and strictly decreases in the Up direction
DODAG Root
  It is the DAG root of the DODAG. The DODAG root may act as a border router for the DODAG, and aggregate routes in the DODAG and may redistribute DODAG routes into other routing protocols.

## Slide 5: RPL topology
DODAG
Up
down
RPL Instance

## Slide 6
Upward path is so common (MP2P)
Downward path is optional mainly for p2p and p2mpp
An RPL instance consists of multiple DODAGs. Traffic moves either up towards the DODAG root or down towards the DODAG leafs